## Slide 1
Department of Mechanical and Manufacturing Engineering
Loughborugh University
APPLICATION OF LES TECHNIQUE
FOR THE CALCULATION OF
INTERNAL COMBUSTION ENGINE FLOWS
EULAG 2012
Ranasinghe R.A.C.P.
Malalasekera W.
Clarke A.

## Slide 2
Department of Mechanical and Manufacturing Engineering
Loughborugh University
LES FOR IC ENGINE SIMULATIONS
LES resolves all the turbulent spectrum larger than the grid scale ( filter scale) & only the sub grid scale motion (SGS) is to be modelled
SGS scales are isotropic and less sensitive to model parameters
Hence LES provides an accurate way to investigate unsteady effects associated with mixture formation, combustion & cyclic variations in IC engines
Present study aims to develop & validate an LES code for IC engine simulations

## Slide 3
Department of Mechanical and Manufacturing Engineering
Loughborugh University
COMPUTATIONAL APPROACH
KIVA 4 RANS code was modified to incorporate LES capability
It uses an arbitrary Lagrangian Eularian approach to solve governing equations in unstructured hexahedron grids with moving boundaries
SGS viscosity was modelled using SGS kinetic energy
Filter width is taken to be the cubic root of the computational cell volume

## Slide 4
Department of Mechanical and Manufacturing Engineering
Loughborugh University
COMPUTATIONAL APPROACH
The following transport equation is solved for
No-slip boundary conditions were imposed on solid walls
Piston motion was modelled by removing and addition of cell layers to minimise the deformation of cells, so that the commutation error is minimum

## Slide 5
Department of Mechanical and Manufacturing Engineering
Loughborugh University
VALIDATION OF KIVA4:LES
FLOW OVER A BACKWARD FACING STEP
Computational mesh & instantaneous U velocity
contour snaps at three instances
Symbols show measured values & lines show simulated results
ER =1.2, Re= 5100 & averaged over 5 flow through times

## Slide 6
Department of Mechanical and Manufacturing Engineering
Loughborugh University
VALIDATION OF KIVA4:LES
FLOW IN AN AXISYMMETRIC ENGINE
RPM= 200 & averaged over 5 cycles
Crank position = 36 ATDC

## Slide 7
Department of Mechanical and Manufacturing Engineering
Loughborugh University
APPLICATION TO SI ENGINE FLOWS
RICARDO E6 ENGINE | 
BORE | 7.62 cm
STROKE | 11.11 cm
RPM | 1800
NO. OF CELLS | 0.8M
RANS RESULTS
LES PREDICTIONS

## Slide 8
Department of Mechanical and Manufacturing Engineering
Loughborugh University
KIVA4:LES is only 2nd order accurate but predictions are in good agreement with experimental measurements
Present LES formulation has been able to resolve most of the energy containing large scale motion
Accuracy of the predictions are quite satisfactory compared to the relative low mesh densities used
CONCLUDING REMARKS
Thank you very much for your cooperation !