## Slide 1: 18th Annual WRF User's Workshop WRF-ARW Research to Operations Update: The Rapid-Refresh (RAP) version 4, High-Resolution Rapid Refresh (HRRR) version 3 and Convection-Allowing Ensemble Prediction
13 June 2017
Curtis Alexander, Steve Weygandt, Stan Benjamin, David Dowell, Ming Hu, Tanya Smirnova, Joseph Olson, Jaymes Kenyon, Georg Grell, Eric James, Haidao Lin, Terra Ladwig, John Brown, Trevor Alcott and Isidora Jankov
NOAA/ESRL/GLOBAL SYSTEMS DIVISION

## Slide 2
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 3
RAP/HRRR Implementation History
RAP/HRRR Implementations
01 May 2012 RAPv1: Adoption of GSI, WRF-ARW and unified post Enabled use of community-developed software | 25 Feb 2014 RAPv2: Hybrid EnKF-3DVar data assimilation Significant improvement in upper-air forecasts
30 Sep 2014 HRRRv1: 3-km Radar DA in WRF-ARW Significant improvement in convective forecasts | 23 Aug 2016 RAPv3/HRRRv2: Aerosol Thompson MP, improvements to MYNN PBL, RUC LSM, RRTMG Rad, Grell-Freitas cumulus Significant improvement in surface forecasts
Operational Implementations
13 Feb 2018
RAPv4/HRRRv3: Hybrid Vertical Coordinate, Eddy Diffusivity Mass Flux PBL
Reduction in short-lead biases and improved mesoscale environment
Extended Forecast Lengths
RAP: 03z, 09z, 15z, 21z 21 hrs  39 hrs
RAP: All other hourly cycles remain 21 hrs
HRRR: 00z, 06z, 12z, 18z 18 hrs  36 hrs
HRRR: All other hourly cycles remain 18 hrs
OCONUS Domains
HRRR-Alaska:
Every 3 hrs to 18 hrs
Every 6 hrs to 36 hrs
HRRR-Hawaii: ??

## Slide 4
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 5
 | Model | Data Assimilation
RAPv4 (13 km) | WRF-ARW v3.8.1+ incl. physics changes Physics changes (12 changes): Thompson microphysics – improved upper-level clouds GF Convective update – more optimal precip bias MYNN PBL update – better sub-grid clouds, meso env LSM update – 15” MODIS data – better lower boundary Refined roughness lengths over various land use types Numerics changes (3 changes): Improved terrain (cell avg) – better winds /turbulence Hybrid vertical coordinate from NCAR – better meso env Full geometric diffusion – better winds/temp in terrain | Merge with GSI trunk – last updated in May 2017 New Observations for assimilation (4 changes): NCEP new VAD wind retrievals AMVs over land and TAMDAR Add IASI, CrIS, SEVIRI radiances Assimilation Methods (9 changes): Revised PBL pseudo-obs – reduce RH bias More ensemble weight in hybrid DA (0.85/0.15) METAR/GOES cloud consistent (<1200m AGL) Cloud building – smaller qc/qi – more retention Reduced latent heating – improved precip bias
HRRRv3 (3 km) | WRF-ARW v3.8.1+ incl. physics changes Physics changes (12 changes): Thompson microphysics – improved upper-level clouds MYNN PBL update – better sub-grid clouds, meso env LSM update – 15” MODIS data – better lower boundary Refined roughness lengths over various land use types Gravity wave drag (RAP and HRRR) – better winds Numerics changes (2 changes): Hybrid vertical coordinate from NCAR – better meso env Full geometric diffusion – better winds/temp in terrain | New Observations for assimilation (5 changes): NCEP new VAD wind retrievals AMVs over land and TAMDAR Radar radial velocity and lightning Assimilation Methods (9 changes): Revised PBL pseudo-obs – reduce RH bias More ensemble weight in hybrid DA (0.85/0.15) METAR and GOES cloud consistent (<1200 m AGL) Cloud building – smaller qc/qi – more retention
RAPv4/HRRRv3 Change Highlights
RAPv4/HRRRv3

## Slide 6
Model | Version | Assimilation | Radar DA | Radiation LW/SW | Microphysics | Cumulus Param | PBL | LSM
RAP | WRF-ARW v3.6+ | GSI Hybrid Ensemble to 0.75 | 13-km DFI | RRTMG/ RRTMG | Thompson Aerosol v3.6 | GF + Shallow | MYNN v3.6 | RUC v3.6
HRRR | WRF-ARW v3.6+ | GSI Hybrid Ensemble to 0.75 | 3-km 15-min LH | RRTMG/ RRTMG | Thompson Aerosol v3.6 | None | MYNN v3.6 | RUC v3.6
Model | Horiz/Vert Advection | Scalar Advection | Upper-Level Damping | Diffusion Option | 6th Order Diffusion | SW Radiation Update | Land Use | MP Tend Limit | Time-Step
RAP | 5th/5th | Positive-Definite | w-Rayleigh 0.2 | Simple (1) | Yes 0.12 | 20 min | MODIS Seasonal | 0.01 K/s | 60 s
HRRR | 5th/5th | Positive-Definite | w-Rayleigh 0.2 | Simple (1) | Yes 0.25 | 15 min with SW-dt | MODIS Seasonal | 0.07 K/s | 20 s
Model | Run at: | Domain | Grid Points | Grid Spacing | Vertical Levels | Vertical Coordinate | Pressure Top | Boundary Conditions | Initialized
RAP | GSD, NCO | North America | 953 x 834 | 13 km | 50 | Sigma | 10 mb | GFS | Hourly (cycled)
HRRR | GSD, NCO | CONUS | 1799 x 1059 | 3 km | 50 | Sigma | 20 mb | RAP | Hourly (pre-forecast hour cycle)
Operational
RAPv3/HRRRv2
RAPv4/HRRRv3 Summary of Changes
RAPv3/HRRRv2

## Slide 7
Model | Version | Assimilation | Radar DA | Radiation LW/SW | Microphysics | Cumulus Param | PBL | LSM
RAP | WRF-ARW v3.8.1+ | GSI Hybrid Ensemble to 0.85 | 13-km DFI, ½ Strength | RRTMG/ RRTMG | Thompson Aerosol v3.8.1 | GF + Shallow | MYNN v3.8.1 | RUC v3.8.1
HRRR | WRF-ARW v3.8.1+ | GSI Hybrid Ensemble to 0.85 | 3-km 15-min LH | RRTMG/ RRTMG | Thompson Aerosol v3.8.1 | None | MYNN v3.8.1 | RUC v3.8.1
Model | Horiz/Vert Advection | Scalar Advection | Upper-Level Damping | Diffusion Option | 6th Order Diffusion | SW Radiation Update | Land Use | MP Tend Limit | Time-Step
RAP | 5th/5th | Positive-Definite | w-Rayleigh 0.2 | Full (2) | Yes 0.12 | 20 min | MODIS Seasonal | 0.01 K/s | 60 s
HRRR | 5th/5th | Positive-Definite | w-Rayleigh 0.2 | Full (2) | Yes 0.25 | 15 min with SW-dt | MODIS Seasonal | 0.07 K/s | 20 s
Model | Run at: | Domain | Grid Points | Grid Spacing | Vertical Levels | Vertical Coordinate | Pressure Top | Boundary Conditions | Initialized
RAP | GSD, NCO | North America | 953 x 834 | 13 km | 50 | Sigma-Isob Hybrid | 10 mb | GFS | Hourly (cycled)
HRRR | GSD, NCO | CONUS | 1799 x 1059 | 3 km | 50 | Sigma-Isob Hybrid | 20 mb | RAP | Hourly (pre-forecast hour cycle)
No Change in CONUS
Domains
Newer Model Version
More Ensemble Weight
Advanced “Physics Suite”
Upcoming
RAPv4/HRRRv3
Seasonal Vegetation
Fraction/Leaf Area Index
RAPv4/HRRRv3 Summary of Changes
RAPv4/HRRRv3

## Slide 8
Hybrid coordinate
Terrain-following coordinate
New RAP/HRRR Vertical Coordinate
Less “Noise” in Hybrid
Hybrid Vertical Coordinate

## Slide 9
RAP RMSE Upper-Air Winter (Three Weeks Jan 2017)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
Temp
RH
Wind
RAPv4
better
RAPv4
better
Upper-Air Verification
Full Tropospheric Improvements

## Slide 10
RAP BIAS Upper-Air Winter (Three Weeks Jan 2017)
00 UTC
12 UTC
RAPv4
RAPv3 (ops)
6 hr fcsts
Temp
RH
Wind
Reduced RH Bias Aloft
Upper-Air Verification

## Slide 11
RAP RMSE Upper-Air Summer (Three Weeks Jul 2016)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
Temp
RH
Wind
RAPv4
better
RAPv4
better
Upper-Air Verification
Full Tropospheric Improvements

## Slide 12
RAP BIAS Upper-Air Summer (Three Weeks Jul 2016)
00 UTC
12 UTC
RAPv4
RAPv3 (ops)
6 hr fcsts
Temp
RH
Wind
Upper-Air Verification

## Slide 13
RAP/HRRR Improved Sub Grid Cloud Effects
Visible Satellite
Experimental HRRRv3
Operational HRRRv2
3hr fcsts
More Shortwave
Attenuation
SURFAD/ISIS DSWRF 6hr Fcst Verification
7D MAE
7D BIAS
3D MAE
3D BIAS
HRRRv3
better
HRRRv3
better
Radiation Verification
Improved Bias

## Slide 14
RAP RMSE Surface Winter (Three Weeks Jan 2017)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
2mT
2mTd
10mWind
RAPv4
better
RAPv4
better
Surface Verification
Improved Diurnal T/Td

## Slide 15
RAP BIAS Surface Winter (Three Weeks Jan 2017)
West US
East US
RAPv4
RAPv3 (ops)
12 hr fcsts
2mT
2mTd
10mWind
Optimal
Optimal
Optimal
Optimal
Optimal
Optimal
Surface Verification

## Slide 16
RAP RMSE Surface Summer (Three Weeks Jul 2016)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
2mT
2mTd
10mWind
RAPv4
better
RAPv4
better
Surface Verification
Improved Daytime T/Td/Wind

## Slide 17
RAP BIAS Surface Summer (Three Weeks Jul 2016)
West US
East US
RAPv4
RAPv3 (ops)
12 hr fcsts
2mT
2mTd
10mWind
Optimal
Optimal
Optimal
Optimal
Optimal
Optimal
Surface Verification

## Slide 18
RAP/HRRR Cloud Building w/Smaller Size Distribution
No
qnr/qni
specified
qnr/qni
specified
at large
values
(small
sizes)
1 hr
1 hr
3 hr
3 hr
4 hr
4 hr
More
low clouds retained
Cloud Verification

## Slide 19
RAP TSS Ceiling Winter (Three Weeks Jan 2017)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
3000’
1000’
500’
RAPv4
better
RAPv4
better
More Skill During Cold/Cloudy Outbreak
6-11 Jan
Ceiling Verification

## Slide 20
RAP TSS Ceiling Summer (Three Weeks Jul 2016)
6 hr
12 hr
RAPv4
RAPv3 (ops)
RAPv4-RAPv3
3000’
1000’
500’
RAPv4
better
RAPv4
better
Ceiling Verification

## Slide 21
RAP CSI/BIAS Precipitation Winter (Three Weeks Jan 2017)
CSI
40 km
BIAS
13 km
RAPv4
RAPv3 (ops)
1 hr
6 hr
12 hr
Optimal
Optimal
Optimal
More Optimal Bias
Precip Verification

## Slide 22
RAP CSI/BIAS Precipitation Summer (Three Weeks Jul 2016)
CSI
40 km
BIAS
13 km
RAPv4
RAPv3 (ops)
1 hr
6 hr
12 hr
Optimal
Optimal
Optimal
More Optimal Bias
Precip Verification

## Slide 23
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 24
Experimental HRRRv3 13 hr fcst
Valid 00 UTC 17 May 2017
Composite Reflectivity Observations
00 UTC 17 May 2017
Operational HRRRv2 13 hr fcst
Valid 00 UTC 17 May 2017
More Accurate
Convection Along
Weakly-Forced Dryline
HRRR Improved Convective Forecasts
Reflectivity Verification

## Slide 25
HRRR CSI/BIAS Precipitation Spring (Three Weeks May 2017)
CSI
40 km
BIAS
3 km
HRRRv3
HRRRv2 (ops)
1 hr
6 hr
12 hr
Optimal
Optimal
Optimal
More Optimal Bias
Precip Verification

## Slide 26
HRRR CSI/BIAS Reflectivity Spring (Three Weeks May 2017)
CSI
40 km
BIAS
3 km
HRRRv3
HRRRv2 (ops)
25 dBZ
30 dBZ
35 dBZ
Optimal
Optimal
Optimal
More Optimal Bias
Reflectivity Verification

## Slide 27
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 28
Ceiling (True Skill Score) HRRR-AK vs NAM-NEST-AK (two weeks)
6 hr
12 hr
3000’
1000’
500’ (rare)
NAM-AK
HRRR-AK
NAM-HRRR
HRRR
better
HRRR
better
HRRR-AK Ceiling

## Slide 29
Visibility (True Skill Score) HRRR-AK vs NAM-NEST-AK (two weeks)
6 hr
12 hr
10 mi
3 mi
1 mi (rare)
NAM-AK
HRRR-AK
NAM-HRRR
HRRR
better
HRRR
better
HRRR-AK Visibility

## Slide 30
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 31
HRRRE 2017 Design
09z
36 HRRRE
members
Ensemble
Kalman Filter
+
Radar Conv Obs
36 HRRRE
Initial Conditions
10z
Sat/ Conv Obs
Ensemble
Kalman Filter
36 1-hr fcsts
Radar Conv Obs
36 HRRRE
Initial Conditions
11z
Sat/ Conv Obs
GSI Soil Adj + Cloud Anal
Ensemble
Kalman Filter
36 1-hr fcsts
Radar Conv Obs
36 HRRRE
Initial Conditions
12z
Sat/ Conv Obs
GSI Soil Adj + Cloud Anal
Stochastic Parameter Perturbation (SPP) PBL - 00z Only
36 1-hr fcsts
GSI Soil Adj + Cloud Anal
DA
Ens
Fcst
Ens
9 HRRRE
18-hr fcsts
3-km interp
RAP Mean
36 GDAS Members
HRRRE Design
HRRR
Soil Moisture Perts

## Slide 32
HRRRE 2017 (01 March – 30 June 2017)
Single core (ARW)
Ensemble DA (DART and GSI-EnKF)
RAP mean + GDAS perturbations w/more inflation
Conventional observations
Radar reflectivity observations
Stochastic physics
Cloud analysis
Soil adjustments
HRRR-TLE post-processing
Assimilation Forecast
36 members 12z – Nine members to 18 hrs
1 hr cycling 15z – Nine members to 18 hrs
15 fcsts / day 18z – Nine members to 18 hrs Start 09z day one 21z – Nine members to 18 hrs
End 00z day two 00z – Nine members to 36 hrs
Proof-of-concept
Real-time demonstration
With NSSL Experimental
WoF System for ensembles
“NEWS-e”
Real-Time Web Graphics
https://rapidrefresh.noaa.gov/hrrr/HRRRE
55% CONUS HRRR
HRRRE Design

## Slide 33
Ensemble Forecast Challenge: Spread vs Error
Isolated Supercell
00z 15 April 2017
Deterministic
HRRR 6-hr
Forecast
More Accurate
Convection with CAM Ensemble DA
in 0-6 hrs
HRRRE Case

## Slide 34
RAP/HRRR: Hourly-Updating Weather Forecast Suite
Initial & Lateral Boundary Conditions
Initial & Lateral Boundary Conditions
13-km Rapid Refresh (RAPv4) – to 39h (Feb 2018)
3-km High-Resolution Rapid Refresh (HRRRv3) – to 36h (Feb 2018)
750-m HRRR nest Scale-ware Physics Testing (ongoing)
3-km Storm-Scale Ensemble Analysis and Forecast (HRRRE) 55% CONUS HRRR Experimental (ongoing)
3-km High-Resolution Rapid Refresh Alaska, Hawaii and Puerto Rico Testing (HRRR-AK, HRRR-HI, HRRR-PR) Experimental (ongoing)
3-km High-Resolution Time Lagged Ensemble (HRRR-TLE)
3-km HRRR-Smoke (VIIRS fire data)
Overview

## Slide 35
RAP/HRRR ESRL/GSD Development Talks
6.1 Wed 10:30 Georg Grell New developments and applications using the scale and aerosol aware Grell-Freitas convection parameterization
P11 Wed 2-5 Isidora Jankov Stochastic Approaches Within a High Resolution Rapid Refresh Ensemble- Part I: Sensitivity Testing
P12 Wed 2-5 Jeff Beck An Evaluation of 3D- and 4D-EnVar Sub-Hourly Data
Assimilation in the HRRR
P34 Wed 2-5 Jaymes Kenyon The MYNN Turbulence Parameterization: Recent Development and Current Capabilities
8.1 Thu 10:30 Jeff Beck An evaluation of the new hybrid vertical coordinate in the RAP and HRRR
8.6 Thu 11:45 Joseph Olson Addressing systematic biases in RAP/HRRR physics for WFIP2
Talks