## Slide 1
Individual and Combined Impacts of Projected Climate and Emission Changes on Future Air Quality over the U.S.
Chinmay Jena1, Yang Zhang1, Kai Wang1, Patrick Campbell1,
Fang Yan2,3, Zifeng Lu 2,3, David Streets2, 3
1Department of Marine, Earth, and Atmospheric Sciences, NCSU, Raleigh, NC
2Computation Institute, University of Chicago, Chicago, IL
3Energy Systems Division, Argonne National Laboratory, Argonne, IL
18th Annual WRF Users' Workshop
Notes: Increase font size for names and also affiliation, they are way too small

## Slide 2
Background and Motivation
Emissions Scenarios
  Special Report on Emissions Scenarios (SRES, 2000)
  Special Report on Emissions Scenarios (SRES, AR4, 2007)
  Representative Concentration Pathways (RCP, AR5, 2014)
But both SRES and RCP scenarios neglecting relationship between socioeconomic factors and projected technology change
  Dynamic Technology Model:
  SPEW-Trend Projections
(Yan et. al., 2014)
Notes: YZ: use the font size 20 for second bullet for consistency
Rapidly increases in modern society activities, economics and population are becoming complex and vulnerable to changes in weather, air quality and climate. Emission projections are critical elements in understanding future climate impacts on regional air quality.
In the past, emission projections have often been estimated by combining fuel consumption with an averaged emission factor that represents the whole emitter population while neglecting relationship between socioeconomic factors and projected technology change. The newly, developed dynamic technology model (Yan et al., 2014) can overcome this deficiency in projecting emissions. This is the model system that uses the dynamic technology model emission projections within the downscaled model system

## Slide 3
P
Projected future energy use
Exogenous scenarios
(e.g. IMAGE and GCAM)
Socioeconomic variables
Relationships that affect
technological changes
IEA energy statistics
(1970-2010)
Fuel consumption
(1970-2050)
Distribution of
engine (all sectors) fuel
consumption by
region/fuel/tech/age
(SPEW-Trend)
Global and regional
emission projections
Emission factor by
species/fuel/tech/age
Technology Driver Model (TDM)
Diagrams of TDM Emission Projection Methods (SPEW-Trend, Yan et. al., 2014)
Gridded Emissions
(SMOKE Model)
Growth Factors
Regions/Sectors/Species
Regional Online Couple Model
(WRF-Chem3.7)
Downscaling Approach
CESM

## Slide 4
Objectives
Impacts on Future Air Quality over the U.S.
from
Emissions Change only
vs.
Climate Change only
vs.
Emissions & Climate Changes

## Slide 5
Domain and Period | 
Model | Online-coupled WRF-Chem 3.7
Period & domain | Current decade 2001-2010 and future decade 2046-2055 over CONUS
Horiz. & Vert. Resolution | 36-km & 34 layers vertically from surface to 100 hPa
WRF-Chem Physics and Chemistry Options | 
Radiation | Rapid and accurate Radiative Transfer Model for GCM (RRTMG)
Land and PBL | National Center for Environmental Prediction, Oregon State University, Air Force and Hydrologic Research Lab (NOAH) and Yonsei University (YSU)
Cumulus | Multi-Scale Kain Fritsch (MSKF)
Microphysics | Morrison 2-moment scheme
Gas-Phase Chemistry | Modified CB05 with updated chlorine chemistry
Aqueous-Phase Chemistry | AQ chemistry module (AQCHEM)
Aerosol Module | Modal Aerosol Dynamics Model/Volatility Basis Set (MADE/VBS)
Photolysis | Fast Troposphere Ultraviolet Visible (FTUV)
Input | 
Meteorological and Chemical (Initial and Boundary Conditions) | Modified CESM/CAM5 v1.2.2 (Glotfelty et al., 2016 a,b) for both meteorology & chemistry; meteorology ICs/BCs bias corrected with NCEP/FNL.
Anthropogenic Emissions Biogenic Emissions Dust and Sea Salt Emissions | U.S. EPA National Emissions Inventory 2002, 2005, 2008 for current decade; TDM-projected growth factor under the IPCC/A1B and B2 scenarios based on 2005 emission; Model of Emissions of Gases and Aerosols from Nature version 2 (MEGAN v2) AER/AFWA (Jones et al., 2012) and Gong et al. (1997) parameterization
Model Configuration

## Slide 6
Simulation Design
Simulation Details | Impacts on Air Quality
Current Climate Current GHG Levels Current emissions | Base Case
Future Climate Future GHG Levels Future emissions | Combined emissions and Climate changes
Current Climate Current GHG Levels Future emissions | Emissions change only
Future Climate Future GHG Levels Future emissions | Climate change only

## Slide 7
Meteorological Performance
MB: -0.6°C, NMB: -4.9%
MB: 0.23 ms-1 , NMB: 6.7%
MB: -1.4%, NMB: -2.0%
MB: 0.04 mm hr-1,
NMB: 57.5%
T2
RH2
WS10
Rain
Precipitation Performance against Satellite/Reanalysis Data
TDM
GPCP
PRISM
TMPA
MB:0.34 mm day-1 ,NMB: 15%
MB: 0.25 mm day,
NMB: 11.7%
MB: 0.35 mm/day,
NMB: 15.5%
Generally cold biases for T2, overprediction of WS10 and RH2 in eastern and mountainous areas of U.S., precipitation overpredicted across the domain

## Slide 8
Simulated O3 and PM2.5 Overlaid with Observations
Ozone
PM2.5
CASTNET: NMB=-8.9%; AQS: NMB=2.3%
IMPROVE: NMB=12.9%; CSN: NMB=6.2%
Overall good performance for O3 (NMB < ±10%), but locally large underpredictions exist in both eastern and western U.S.; PM2.5 performs well in eastern U.S., but there are larger negative biases in western U.S.

## Slide 9
Projected Emission Changes
TDM A1B Scenario
Abs. changes
Rel. changes
Under the A1B scenario, emissions of CO, NOX, VOCs, and PM2.5 are projected to decrease over large areas of domain with a few exceptions (e.g., Florida and Ohio River)
TDM B2 Scenario
Under the B2 scenario, emissions of CO, NOx, VOCs, and PM2.5 are projected to decrease over large areas of domain with a few exceptions (e.g., Ohio River)
CO
NOX
VOC
PM2.5
Notes: “with a few exceptions Ohio River” does not make sense, did you mean
with a few exceptions (e.g., Ohio River)

## Slide 10
TDM/A1B
TDM/B2
Emissions
Change only
Climate
Change only
Emissions and
Climate Changes
Projected Air Quality Changes
Daily Maximum 8-hr Avg. O3
Daily 24-hr Avg. PM2.5
The maximum daily 8-h average surface ozone (MDA8h O3) increases by ~3 ppb across the U.S. due to (i) enhanced CH4 concentrations and subsequent higher T2, (ii) increased biogenic VOC emissions, and (iii) larger NOx emission reduction than VOC emission reduction over VOC-limited regions
The daily 24-h average (DA24h) PM2.5 levels are projected to decrease over eastern U.S., mainly due to the decreases in primary anthropogenic emissions of PM species and gaseous precursors and secondary formation of inorganic aerosols as well as increased precipitation

## Slide 11
TDM/A1B
TDM/B2
Emissions
Change only
Climate
Change only
Emissions and
Climate Changes
Number of exceedance days for MDA8h Ozone > 70 ppb
Number of exceedance days for daily 24-hr Avg. PM2.5 > 35 µg m-3
The number of exceedance days (MDA8h O3 > 70 ppb) is significantly reduced in emission change only scenario but increased in climate change only scenario. Overall changes in number of exceedance days are dominant by emission change only scenario
The number of exceedance days DA 24hr PM2.5 > 35 µg m-3 is significantly reduced over eastern U.S.

## Slide 12
Conclusions
The model shows overall good performance for meteorological variables, O3 and PM2.5 over CONUS
The maximum daily 8-h average surface ozone (MDA8h O3) increases by ~3 ppb across the U.S. The number of exceedance days (MDA8h O3 > 70 ppb) is significantly reduced but some areas remain non-attainment
The daily 24-h average (DA24h) PM2.5 levels are projected to decrease over eastern U.S. The number of exceedance days (DA24hr PM2.5 > 35 µg m-3) is significantly reduced over eastern U.S.
The climate change dominates the changes in surface O3 concentration under the TDM A1B scenario across the CONUS, while the changes in anthropogenic emissions dominate surface O3 levels under the TDM B2 scenario and PM2.5 under both TDM A1B and B2 scenarios
The results will be useful for policy makers to develop integrated strategies to control anthropogenic emissions and mitigate adverse climate change

## Slide 13
The National Science Foundation EaSM program (AGS-1049200) at NCSU and the USDA EaSM program (2012-67003-30192) at the University of Chicago/ANL
High performance computing support from Yellowstone (ark:/85065/d7wd3xhc) provided by NCAR’s Computational and Information Systems Laboratory, sponsored by the National Science Foundation; and from Stampede, provided as an Extreme Science and Engineering Discovery Environment (XSEDE) digital service by the Texas Advanced Computing Center (TACC) (http://www.tacc.utexas.edu), which is supported by National Science Foundation grant number ACI-1053575
Acknowledgments