## Slide 1: A high-altitude wind power (HAWP) climatology with global WRF
Mark Stoelinga, James McCaa, and Rhea George

## Slide 2: High altitude wind power (HAWP)
0
500

## Slide 3: High altitude wind power (HAWP)
0
500

## Slide 4: High altitude wind power (HAWP)
Here’s where the gold is, if you can reach it. Wind resource is:
Stronger
Steadier
Less turbulent
0
500

## Slide 5: Novel technologies

## Slide 6: Wind Resource Assessment Mapping
Designed for “prospecting” wind energy
A “light” version of regional climate modeling:
  Primary interest is recent climate
  Relies on downscaling of global reanalysis datasets
  Fewer freely forecasted aspects
  Periodically reinitialized (every N days, N = 3 to 30)
    Maintain fidelity to reanalysis
    Parallelization in time

## Slide 7: 2007: 3TIER’s “FirstLook”
Global, 5-km resolution
10-year climatology
But….
Turbine hub-height winds
NCEP/NCAR Reanalysis
WRF V2
Simple nudging

## Slide 8: And…no global WRF

## Slide 9: What did we want this time? How did we get there?
Global coverage including oceans: Global WRF V3.7.1
Avoid tiling and blending: Global WRF V3.7.1
More output variables, higher altitude: More storage
Better reanalysis: ERA-Interim
Better downscaling: Spectral Nudging
Higher resolution but faster production: Mass-conserving diagnostic flow model (10 km  2 km)
Other configuration options: YSU PBL, Ferrier micro, RRTMG radiation

## Slide 10: Global WRF
Derived from PlanetWRF
Major modifications:
  Unequal map scale factors in x and y directions  allows for global lat/lon grid
  Polar filter: northern and southern boundaries collapse to single point, requiring special treatment

## Slide 11: Why not MPAS?
Experience with WRF
Physics options
Continuous mesh refinement not really needed
Spectral nudging required for reanalysis (or climate model) downscaling.
However, in the future…

## Slide 12: Tribulations with Global WRF
Two bugs encountered in Global WRF (V3.6.1)
  Polar filter generating negative mixing ratios
  Polar point instability
  Discovered and fixed both by us and WRF team in V3.7
Recurrent problems with interactions between:
  Adaptive timestep
  Restarts
  ESMF
  Delayed nests (not for global)

## Slide 13: Finally, success!
Note, speeds over ocean reduced by 1/2
5-day, hourly loop of 50-m wind speed

## Slide 14: 10-year mean wind speed, 50 m

## Slide 15: 10-year mean wind speed, 150 m

## Slide 16: Ratio, 150-m to 50-m wind speed