## Slide 1: Combined Impacts of Nitrous Acid and Nitryl Chloride on Lower Tropospheric Ozone: New Module Development in WRF-Chem and Application to China
Li Zhang1, Qinyi Li1, Tao Wang1, Ravan Ahmadov2, 3, Qiang Zhang4, and Meng Li4
1 Department of Civil and Environmental Engineering, The Hong Kong Polytechnic University, Hong Kong, China,
2Cooperative Institute for Research in Environmental Sciences, University of Colorado at Boulder, Boulder, CO, USA,
3Earth System Research Laboratory, National Oceanic and Atmospheric Administration, Boulder, CO, USA,
4Department of Earth System Science, Tsinghua University, Beijing, China
12-16 JUNE 2017, BOULDER, CO
18TH ANNUAL WRF USERS' WORKSHOP:

## Slide 2: Outline
Background
Model developments on HONO and Chlorine chemistry
Simulations of HONO and ClNO2
Impact on tropospheric ozone in China
Summary

## Slide 3: Introduction: HONO and N2O5/ClNO2 processes
NO2
NO
O3
hν
RO2, HO2
Daytime
O3
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 4
NO2
NO
O3
hν
RO2, HO2
Daytime
HONO
Ground
OH
Emission
O3
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 5
NO2
NO
O3
hν
RO2, HO2
Daytime
HONO
OH
Ground
OH
Emission
O3
hν
oxidation
VOCs
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 6
NO2
NO
OH
O3
hν
RO2, HO2
Daytime
HNO3 + NO3-
HONO
OH
Ground
OH
Emission
O3
hν
oxidation
VOCs
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 7
NO2
NO
OH
O3
hν
RO2, HO2
Daytime
HNO3 + NO3-
HONO
OH
Ground
OH
Emission
O3
hν
6%-10% enhancement in O3 over HK-PRD due to HONO sources/processes
Without HONO sources
With HONO sources
oxidation
VOCs
Comprehensive HONO sources (heterogeneous formations on various surfaces; gas-phase formations; oceanic source; traffic emissions; soil bacterial emissions) were considered into CBMZ_MOSAIC (Zhang et al., 2016, JGR)
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 8: Introduction: HONO and N2O5/ClNO2 processes
NO2
NO
NO3
O3
NO2
M
O3
hν
NO
Nighttime
N2O5
Daytime
ClNO2
Cl-
O3
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 9
NO2
NO
NO3
O3
NO2
M
O3
hν
NO
Nighttime
N2O5
Cl•
O3
Oxidation
VOCs
Daytime
ClNO2
Cl-
O3
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 10
NO2
NO
NO3
O3
NO2
M
O3
hν
NO
Nighttime
N2O5
Cl•
O3
Oxidation
VOCs
Daytime
H2O
ClNO2
Cl-
HNO3 + NO3-
VOCs
O3
OH
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 11
OH
NO2
NO
NO3
O3
NO2
M
O3
hν
NO
Nighttime
N2O5
Cl•
O3
Oxidation
VOCs
Daytime
H2O
ClNO2
Cl-
HNO3 + NO3-
VOCs
O3
Impacts on Total nitrate (μg m-3)
Impacts on Ozone (ppb)
Significant Impacts of N2O5 uptake and ClNO2 production on total nitrate (13.45 μg m-3) and ozone (7.23 ppb) in the HK-PRD
Incorporation of ISORROPIA II & heterogeneous processes of N2O5/ClNO2 into MADE/VBS; Cl-initiated reactions in RACM_ESRL (Li et al., 2016, ACP)
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 12: Closer look at the HONO and N2O5/ClNO2 processes
Competition between HONO and N2O5 processes.
  Both of them change the partitioning of reactive nitrogen.
Emitted/formed during different period
  HONO is emitted/formed both in the daytime and night-time.
  N2O5 and ClNO2 is produced in the night-time.
Emitted/formed from different regions and at different altitudes.
  HONO can be emitted/formed in urban and rural regions
  HONO can be emitted from the surface and formed aloft.
  ClNO2 is produced where N2O5 is concentrated, which is generally the immediate downwind region of urban areas
  N2O5 is also elevated in the residual layer.

## Slide 13
NO2
NO
OH
NO3
O3
NO2
M
O3
hν
RO2, HO2
NO
Nighttime
N2O5
Cl•
O3
Oxidation
VOCs
Daytime
H2O
ClNO2
Cl-
HNO3 + NO3-
VOCs
HONO
OH
Ground
OH
Emission
O3
hν
oxidation
VOCs
What if we consider HONO and ClNO2 simultaneously?
Notes: • Nitrous acid (HONO) is a major source of the hydroxyl radical (OH) in the polluted troposphere (Su et al., 2011). The heterogeneous uptake of dinitrogen pentoxide (N2O5) produces the particulate nitrate and the nitryl chloride (ClNO2) hence the chlorine radical (Cl) (Brown et al., 2006; Osthoff et al., 2008).
• The OH and Cl radical initiate the degradation of volatile organic compounds which results in the ozone formation (Atkinson et al, 2000; Thornton et al., 2010).
• The HONO and N2O5 process, therefore, influence the surface ozone and total nitrate formation.
• Photochemical (ozone) and haze (particulate) pollution has raised huge concerns in China in recent years. However, the collective role of HONO, N2O5 and ClNO2 chemistry in the formation of air pollution in China is not quantified.
•

## Slide 14
These important chemistry affecting the atmospheric oxidation capacity have been missing in many CTMs !
O3 & SA
ClNO2
HONO
N2O5
NO3
NO2
NO
HNO3
OH
Cl·
Cl-
hν
O3
hν
OH
hν
emission
emission
emission
surface
hv
O3, RO2, HO2
NO2
hν
surface
NO
Motivation:
1. To complete this part of reactive nitrogen chemistry in WRF-Chem; 2. To investigate their impacts on secondary pollutants (e.g. ozone)

## Slide 15: Reactive Nitrogen Oxides Mechanism (CBMZ_ReNOM)
Gas phase chemistry
Chlorine chemistry
Aerosol phase chemistry
Heterogeneous uptake of N2O5 and NO2 on aerosol and/or land surface to produce ClNO2 and HONO
Photolysis
Chlorine species
Emission
HONO emission from soil and traffic
CBMZ-MOSAIC module in WRF-Chem
Details and validations are referred to Zhang et al. 2017, ACP, in review
Notes: In this study, we use a revised version of the WRF-Chem model, which includes…
Weather Research and Forecasting model coupled with Chemistry (WRF-Chem) has been incorporated with comprehensive reactive nitrogen oxides mechanism (ReNOM), including the latest HONO sources, the heterogeneous uptake of N2O5 and the subsequent ClNO2 production and chlorine chemistry (Zhang et al., in preparation).
The CBMZ-MOSAIC module (Archer-Nicholls et al., 2014) in WRF-Chem was further developed to include the emission and heterogeneous production of HONO (Zhang et al., 2016) and the gas phase chlorine chemistry (Sarwar et al., 2012), see Fig 2.
Original and updated WRF-Chem were then used to conduct simulations to model the abundance of HONO and ClNO2, and to evaluate the impacts of model developments on air pollutants. Simulations were conducted in different setups, as shown in Table 1, in which MEIC and EDGAR emission inventory were used for China and other Asia regions, respectively, and RECI-China is reactive chlorine emission developed based on coal and biomass burning. All cases modeled air flow and air pollutants from July 1 to 31, 2014, focusing China.

## Slide 16
HONO Chemistry Development
1. Heterogeneous formations & gas-phase reactions of HONO were added into the CBMZ_ReNOM.
2. Traffic & Biological emissions of HONO were also considered.
(Zhang et al., 2017, ACP, in review)

## Slide 17
No. | Reaction | Reaction rate
01 | Cl2 + hvCl + Cl | 
02 | HOCl + hvCl + OH | 
03 | ClNO2 + hvCl + NO2 | 
04 | ClONO2 + hvCl + NO3 | 0.83×
05 | ClONO2 + hvClO + NO2 | 0.17×
06 | FMCl + hvCl + CO + HO2 | 
07 | FMCl + OHCl + CO + H2O | 5.0 × 10−13
08 | HCl + OHCl + H2O | ARRH(1.7 × 10-12, -230.0)
09 | Cl2 + OHHOCl + Cl | ARRH(3.6 × 10-12, -1200.0)
10 | HOCl + OHClO + H2O | 5.0 × 10-13
11 | ClO + ClO0.3 Cl2 + 1.4 Cl + O2 | 1.63 × 10-14
12 | ClO + NO2ClONO2 | 7.0 × 10-11
13 | ClO + NOCl + NO2 | ARRH(6.4 × 10-12, 290.0)
14 | ClO + HO2HOCl + O2 | ARRH(2.7 × 10-12, 220.0)
15 | ClO + OHHO2 + Cl | 1.8 × 10-11
16 | ClO + OHHCl + O2 | 1.2 × 10-12
17 | Cl + O3ClO + O2 | ARRH(2.3 × 10-11, -200.0)
18 | Cl + NO2ClNO2 | TROE(1.8 × 10-31, 2.0, 1.0 × 10-10, 1.0)
19 | Cl + HO2HCl + O2 | 3.5 × 10−11
20 | Cl + HO2ClO + OH | ARRH(7.5 × 10-11, -620.0)
21 | Cl + H2O2HCl + HO2 | ARRH(1.1 × 10-11, -980.0)
22 | Cl + NO3NO2 + ClO | 2.4 × 10−11
23 | Cl + ClONO2Cl2 + NO3 | ARRH(6.2 × 10-12, 145.0)
24 | Cl + CH4HCl + CH3O2 | ARRH(6.6 × 10-12, -1240.0)
25 | Cl + C2H6HCl + 0.991 ALD2 + XO2 + HO2 | ARRH(8.3 × 10-11, -100.0)
26 | Cl + PARHCl + XO2 + 0.11 HO2 + 0.06 ALD2 + 0.11 PAR + 0.76 RO2 | 5.0 × 10−11
27 | Cl + ETHFMCl + 2 XO2 + HO2 + HCHO | 1.07 × 10−10
28 | Cl + OLEFMCl + 0.33 ALD2 + 2 XO2 + HO2 + PAR | 2.5 × 10−10
29 | Cl + OLI0.3 HCl + 0.7 FMCl + 0.45 ALD2 + 0.3 OLE + 0.3 PAR + 1.7 XO2 + HO2 | 3.5 × 10−10
30 | Cl + ISOP0.15 HCl + XO2 + HO2 + 0.85 FMCl+ISOPRD | 4.3 × 10−10
31 | Cl + HCHOHCl + HO2 + CO | ARRH(8.2 × 10-11, -34.0)
32 | Cl + ALD2HCl + C2O3 | 7.9 × 10−11
33 | Cl + CH3OHHCl + HO2 + HCHO | 5.5 × 10−11
34 | Cl + ANOLHCl + HO2 + ALD2 | ARRH(8.2 × 10-11, 45.0)
35 | Cl + TOLHCl + 0.88 XO2 + 0.88 HO2 + 0.12 NAP | 6.1 × 10−11
36 | Cl + XYLHCl + 0.84 XO2 + 0.84 HO2 + 0.16 NAP | 1.2 × 10−10
No. | Reaction | Reaction rate
01 |  | 
02 |  | 
03 |  | 
04 |  | 
05 |  | 
06 |  | 
07 |  | 5.0 × 10−13
08 |  | ARRH(1.7 × 10-12, -230.0)
09 |  | ARRH(3.6 × 10-12, -1200.0)
10 |  | 5.0 × 10-13
11 |  | 1.63 × 10-14
12 |  | 7.0 × 10-11
13 |  | ARRH(6.4 × 10-12, 290.0)
14 |  | ARRH(2.7 × 10-12, 220.0)
15 |  | 1.8 × 10-11
16 |  | 1.2 × 10-12
17 |  | ARRH(2.3 × 10-11, -200.0)
18 |  | TROE(1.8 × 10-31, 2.0, 1.0 × 10-10, 1.0)
19 |  | 3.5 × 10−11
20 |  | ARRH(7.5 × 10-11, -620.0)
21 |  | ARRH(1.1 × 10-11, -980.0)
22 |  | 2.4 × 10−11
23 |  | ARRH(6.2 × 10-12, 145.0)
24 |  | ARRH(6.6 × 10-12, -1240.0)
25 |  | ARRH(8.3 × 10-11, -100.0)
26 |  | 5.0 × 10−11
27 |  | 1.07 × 10−10
28 |  | 2.5 × 10−10
29 |  | 3.5 × 10−10
30 |  | 4.3 × 10−10
31 |  | ARRH(8.2 × 10-11, -34.0)
32 |  | 7.9 × 10−11
33 |  | 5.5 × 10−11
34 |  | ARRH(8.2 × 10-11, 45.0)
35 |  | 6.1 × 10−11
36 |  | 1.2 × 10−10
2. Seven new chlorine species were introduced into CBMZ_ReNOM (Cl, Cl2, ClO, HOCl, ClNO2, ClONO2, and FMCl); six new photolysis reactions in Fast-J and Madronich modules
1. Heterogeneous processes of N2O5 were in the modified MOSAIC by Archer-Nicholls et al., 2015 (GMD)
Chlorine Chemistry Development
3. Mechanism of chlorine chemistry was added， including photolysis, gas-phase reactions with trace gases and VOCs
(Zhang et al., 2017, ACP, in review)

## Slide 18: Simulation cases
Simulation cases | Descirption | Emission Inventory
BASE | Default model | MEIC+MICS
ReNOM_HONO | Only additional HONO | MEIC+MICS+RCEI
ReNOM_Cl | Only Chlorine chemistry | MEIC+MCIS+RCEI
ReNOM | Both HONO and Chlorine chemistry | MEIC+MICS+RCEI
Notes: The revised WRF-Chem was adopted to simulate the spatial-temporal distribution of HONO and ClNO2, and to investigate the contribution of nitrogen chemistry to the production of ozone and secondary nitrate in China in summer when photochemical pollution is severe, and to explore the impacts of nitrogen chemistry on the O3 sensitivity on NOx and VOC emission.

## Slide 19
Model Performance: spatial distributions
HONO was concentrated over the NCP, YRD, and PRD regions, with levels of 800–1800 ppt at ground-level; N2O5 and ClNO2 were abundant over the NCP, YRD, central China, and Sichuan Basin (where with intensive anthropogenic emissions of NOx and chloride with average concentrations of 100–160 ppt and 800–1200 ppt, respectively.

## Slide 20
HONO was concentrated at the surface (as its main precursor NO2)
N2O5 and ClNO2 were most abundant within the 0–600 m (its formation significantly occur within the residual layer during nighttime; downward mixing during morning)
Model Performance: vertical distributions

## Slide 21
Figure S3. Observed and simulated (a) NO2, (b) HONO, (c) N2O5 and (b) ClNO2 at the Wangdu site during the simulation period (27 Jun - 7 Jul 2014).
Detailed comparison against measurements in a intensive field campaign (CareBeijing 2014)
Very good simulations of HONO (well captures the diurnal patterns and averages of the HONO observation)
Satisfactory performances in N2O5 and ClNO2 (overestimates during 1-7 Jun 2014 due to oversitmates in NO, incomplete consideration of sinks, and uncertainties in emission)
NO2
HONO
N2O5
ClNO2

## Slide 22: Overall, the module offers satisfactory simulations of HONO, N2O5, and ClNO2 over Asia (compared with the observations in China, Taiwan, Korea, and Japan)
Comparison against measurements in multiple regions in Asia

## Slide 23: Impacts on Ozone
Significant improvements in ozone predictions (~900 sites):
MB: -4.3 ppb --> 0.1 ppb
Noticeable impacts on lower tropospheric ozone over polluted regions in China
Zhang, L., et al., 2017, ACP, in review
6-13% at surface
3-6% in PBL

## Slide 24: Improvements in O3 prediction: Statistics
Region | Case | No. OBS | OBS | MOD | COR | MB | RMSE | NMB | NME
 | BASE | 49789 | 47.2 | 37.3 | 0.60 | -9.9 | 26.8 | -20.9% | 44.0%
 | ReNOM_Cl |  |  | 40.0 | 0.61 | -7.2 | 26.7 | -15.3% | 43.7%
NCP | ReNOM_HONO |  |  | 41.2 | 0.61 | -6.0 | 26.4 | -12.7% | 43.3%
 | ReNOM |  |  | 43.5 | 0.61 | -3.6 | 26.5 | -7.7% | 43.5%
 | BASE | 34857 | 31.5 | 36.8 | 0.56 | 5.2 | 29.3 | 16.6% | 68.2%
 | ReNOM_Cl |  |  | 39.4 | 0.56 | 7.9 | 31.9 | 25.1% | 72.7%
YRD | ReNOM_HONO |  |  | 43.3 | 0.54 | 11.8 | 34.3 | 37.3% | 77.5%
 | ReNOM |  |  | 45.3 | 0.54 | 13.8 | 36.3 | 43.8% | 81.7%
 | BASE | 15627 | 25.0 | 15.6 | 0.53 | -9.4 | 28.0 | -37.6% | 75.8%
PRD | ReNOM_Cl |  |  | 15.6 | 0.53 | -9.4 | 27.9 | -37.6% | 75.8%
 | ReNOM_HONO |  |  | 18.5 | 0.54 | -6.4 | 26.3 | -25.8% | 73.7%
 | ReNOM |  |  | 18.4 | 0.54 | -6.5 | 26.3 | -26.1% | 73.9%
 | BASE | 214596 | 35.3 | 31.0 | 0.51 | -4.3 | 27.3 | -12.2% | 57.5%
 | ReNOM_Cl |  |  | 32.6 | 0.51 | -2.8 | 28.0 | -7.8% | 58.5%
China | ReNOM_HONO |  |  | 34.1 | 0.52 | -1.2 | 26.7 | -3.5% | 56.6%
 | ReNOM |  |  | 35.5 | 0.52 | 0.1 | 26.1 | 0.4% | 55.8%
Noticeably improved the predicted ozone in China, especially over the NCP and PRD
~900 stations

## Slide 25: Summary
1. Introduction
2. Methodology
3. Results
4. Summary
4. Summary
We made several developments (CBMZ_ReNOM) in WRF-Chem to comprehensively consider processes/emissions of HONO and Chlorine chemistry.
ReNOM is able to satisfactorily simulate the observed HONO and ClNO2.
ReNOM gives better predictions of O3 in China, especially in the NCP and PRD regions.
HONO and ClNO2 significantly enhanced the ozone pollution in China, and the combined effects of them were larger their linear sums

## Slide 26: What’s Next…
To update the Chlorine Emission Inventory in China
To investigate these “new” reactive nitrogen chemistry’s impacts on ozone control strategy (VOC-limited or NOx-limited)
Impacts on PM2.5 (e.g. Nitrate)
More tests & Will contribute the codes to the next release of WRF-Chem (now upon request)

## Slide 27: Acknowledgement
The authors are grateful to financial support from The Hong Kong Polytechnic University, the Hong Kong Research Grant Council, and the National Natural Science Foundation of China.
Thanks to Peking University for the measurement data from CareBeijing 2014 Campaign.
Thanks to Dr. Y.J. Tham at University of Helsinki and Dr. Z. Xu at Nanjing University.

## Slide 28
Thanks for your attention.
L. Zhang: alex.zhang@connect.polyu.hk

## Slide 29: APPENDIX

## Slide 30
Zhang et al., 2017, ACPD
Zhang et al., JGR, 2016;
Li et al., ACP, 2016
HONO chemistry
HONO emission
NO2 -heterogeneous
HONO Uptake
Gas-phase sources
N2O5 & ClNO2 Chemistry
Chloride emission
N2O5 -heterogeneous
ClNO2 production
Cl reactions
Reactive Nitrogen Oxides Mechanism (ReNOM)
CBMZ-MOSAIC and RACM-SOA-VBS
CBMZ-ReNOM and RACM-ReNOM

## Slide 31
Enhancements in ground-level ozone
ReNOM_HONO
ReNOM_Cl
ReNOM
6-13% enhancements over polluted regions

## Slide 32
Region | Case | Daily |  | 8 h Maximum |  | 1 h Maximum | 
 |  | Enhancement | Ratio | Enhancement | Ratio | Enhancement | Ratio
NCP | ReNOM_Cl | 0.64 | 2.3% | 0.77 | 2.1% | 0.78 | 2.0%
 | ReNOM_HONO | 1.14 | 4.1% | 1.43 | 3.8% | 1.43 | 3.7%
 | ReNOM | 1.93 | 7.0% | 2.39 | 6.4% | 2.40 | 6.3%
 | ReNOM_Cl | 0.03 | 0.2% | 0.03 | 0.2% | 0.03 | 0.2%
YRD | ReNOM_HONO | 1.33 | 9.5% | 1.78 | 9.8% | 1.86 | 10.1%
 | ReNOM | 2.13 | 15.3% | 2.89 | 15.9% | 3.03 | 16.4%
 | ReNOM_Cl | 0.02 | 0.2% | 0.02 | 0.1% | 0.02 | 0.1%
PRD | ReNOM_HONO | 1.02 | 9.6% | 1.30 | 9.9% | 1.31 | 9.9%
 | ReNOM | 1.70 | 15.9% | 2.15 | 16.3% | 2.16 | 16.3%
Whole Domain | ReNOM_Cl | 0.31 | 2.0% | 0.39 | 1.9% | 0.40 | 1.9%
 | ReNOM_HONO | 0.81 | 5.2% | 1.03 | 5.0% | 1.01 | 4.7%
 | ReNOM | 1.35 | 8.6% | 1.71 | 8.3% | 1.70 | 7.9%
Enhancements in ground-level ozone: statistics

## Slide 34
ReNOM_Cl
Impact on ozone: vertical distributions
ReNOM
ReNOM_HONO

## Slide 35
BASE
ReNOM
Improvements in O3 prediction: MOD-OBS

## Slide 36
NO2 Performance

## Slide 37
Figure S2. (a) Spatial and (b) vertical distributions of nighttime chloride (μg m-3) during the simulation period.

## Slide 38: HONO and ClNO2 simulation from revised WRF-Chem
Average of daily-maximum
Significant HONO (> 1ppb) over city-cluster and some rural areas
Significant ClNO2 (> 0.3 ppb) over city-cluster and its immediate downwind area
Higher in winter than in summer. Possible causes?
Notes: The simulated HONO from the ReNOM case concentrated (>1 ppb) in major city clusters, including Northern China Plain (NCP), Yangtze River Delta (YRD), Pearl River Delta (PRD), central China (CC) and Sichuan basin (SC) for traffic emission and heterogeneous production, and some rural areas for intensive soil emission at surface level. As to the HONO within the PBL, the WRF-Chem results showed lower concentration.
• The ClNO2 modelled in the ReNOM case demonstrated noticeable levels (>0.3 ppb) in NCP, YRD, CC and SC regions at surface level. As for the ClNO2 concentrations within the PBL, the ReNOM case modeled higher levels compared to those at surface.

## Slide 39: Impacts on ozone
Elevated O3 (> 70 ppb) simulated over city-clusters in summer
Significant impacts (> 10 ppb) on O3 in both summer and winter, contributing to the formation of photochemical pollution
Higher impact in winter
Notes: • The ReNOM case predicted elevated concentrations of O3 and total nitrate especially in the five city clusters.
• The simulated O3 and total nitrate at surface level were higher than those within the PBL.
• The HONO and N2O5 processes increased the O3 formation in the urban area due to the extra source of OH and Cl radicals, suggesting the role of reactive nitrogen processes in the photochemical ozone pollution.
• The HONO and N2O5 chemistry significantly enhanced the formation of total nitrate, especially in the NCP region, which implies the potential importance of reactive nitrogen chemistry in the haze formation.

## Slide 40: Implications for ozone control strategy
HONO and N2O5/ClNO2 chemistry reshapes the O3 sensitivity to the NOx and VOC emission.
Need to consider the new sources/processes of reactive nitrogen in ozone control strategy formulation.
Notes: • With the WRF-Chem model incorporated with reactive nitrogen chemistry, the sensitivity of surface O3 to NOx emission significantly decreased in NCP, YRD, PRD, and major cities in China due to the addition of new radicals, and varied in the rural areas: increased in central China and decreased in southern China, probably due to difference of the HONO emission from soil.
• The sensitivity of O3 to VOC emission increased in the urban area possibly attributed to the new source of OH and Cl radicals.
• The sensitivity of O3 to NOx and/or VOC emissions in a significant portion of the region will change if the reactive nitrogen chemistry is considered.